## Slide 1: Glass
Presenters:
Alejandra Carrillo
Loredana Neves

## Slide 2: Index
Introduction
Content
  History of glass
  Concept
  How it is produced
  Characteristics
  Techniques
  Types
  Importance
Conclusion
References

## Slide 3: Introduction
Glass is a material that we use every day, as decoration and for specific functions such as protection like windows.
There is such a wide variety of types.
  Glass is an extremely versatile material: it can be blown, molded, cut, twisted, colored, transparent, or opaque.
  Also, glass can be made into numerous forms: bowls, glasses, vases, and ink wells.
One of the most appealing things about glass is the range of colors.

## Slide 4: History of glass
Timeline
2400 B.C
2500 B.C
0
12th A.C
19th A.C
17th A.C

## Slide 5: History of glass
Timeline
2400 B.C
2500 B.C
0
12th A.C
19th A.C
17th A.C
Mesopotamia
Manufacture of glass vessels
It is believed that glass was accidently discovered by potters experimenting with glazes for pottery.

## Slide 6: History of glass
Timeline
2400 B.C
2500 B.C
0
12th A.C
19th A.C
17th A.C
Egypt
Glass objects

## Slide 7: History of glass
Timeline
2400 B.C
2500 B.C
0
12th A.C
19th A.C
17th A.C
Rome
Lack of transparency led to stained glass
They discovered “colorless” glass by adding manganese oxide.

## Slide 8: History of glass
Timeline
2400 B.C
2500 B.C
0
12th A.C
19th A.C
17th A.C
France
Introduced plate glass: large sheets of glass became practicable

## Slide 9: History of glass
Timeline
2400 B.C
2500 B.C
0
12th A.C
19th A.C
17th A.C
Mechanization of glass

## Slide 10: Concept
Glass is an amorphous (non-crystalline) solid material.
They are a hard material and optically transparent.
It is composed mainly of sand and alkali.

## Slide 11: How it is produced
1. These materials sand (silicates, SiO2) and an alkali at high temperature fuse together.
2. They are cooled rapidly forming a rigid structure, however not having enough time to form a crystalline regular structure.

## Slide 12: How it is produced
Common ingredients to obtain glass:
Sand
(SiO2 silica)
In its pure form it exists as a polymer.
Normally SiO2 softens up to 2000°C, where it starts to degrade. Adding soda will lower the melting point to 1000°C making it more manageable.
Soda ash
(sodium carbonate Na2CO3)
Also known as lime, calcium carbonate is found naturally as limestone, marble, or chalk. The soda makes the glass water-soluble, soft and not very durable. Therefore lime is added increasing the hardness and chemical durability and providing insolubility of the materials.
Limestone
(calcium carbonate or CaCo3) or dolomite (MgCO3)
Other materials and oxides can be added to increase properties (tinting, durability, etc.), produce different effects, colors, etc.

## Slide 13: Characteristics
Solid and hard material
Disordered and amorphous structure
Fragile and easily breakable into sharp pieces
Transparent to visible light
Inert and biologically inactive material.

## Slide 14: Characteristics
Is 100% recyclable and one of the safest packaging materials due to its composition and properties
It is used for:
Architecture application
Illumination
Electrical transmission
Instruments for scientific research
Optical instruments
Domestic tools
Even textiles.
Glass does not deteriorate, corrode, stain or fade the safest packaging materials.
These properties can be modified and changed by adding other compounds or heat treatment

## Slide 15
In its molten state is usually either blown or molded.
These two methods date back to ancient times and have changed little over the years.
  Blown Glass: Glass is gently blown through an iron rod to create a “bubble” of glass. Different shapes are made and manipulated by spinning or swinging the glass form or with the use of different tools.
  Molded Glass: Ancient glass makers used clay molds to form molten glass. In the 19th century, English glass makers developed methods to mass produce molded glass. Pressed glass is a particular type of molded glass
Techniques

## Slide 16
Most common commercial glass and less expensive
Composition: 60-75% silica, 12-18% soda, and 5-12% lime
Smooth and nonporous surface: allows glass bottles and packaging glass to be easily cleaned.
Glass containers are resistant to chemical attack from aqueous solutions so they will not contaminate the contents inside or affect the taste.
Does not allow light at a wavelength of lower than 400 nm (UV light) to pass.
Uses: bottles, jars, everyday drinking glasses, and window glass.
Light transmission
to be use in flat glass of windows.
Commercial glass or Soda-lime glass
Disadvantages: not resistant to high temperature and thermal changes

## Slide 17: Types
Lead Glass
Composition: 54-65% SiO2, 18-38% lead oxide, 13-15% soda or potash
In moderate amounts: increases durability
In high amounts: lowers the melting point and decreases the hardness giving a soft surface
High refractive index giving high brilliance glass
These properties make it appropriate for decorating purposes
Glass with high lead oxide contents may be used as radiation shielding glass
It doesn’t withstand high temperatures or sudden changes in temperature

## Slide 18
Borosilicate glass
Composition: silica (70-80%), boric oxide (7-13%) and smaller amounts of the alkalis such as 4-8% of Na2O and K2O, and 2-7% aluminum oxide.
Boron gives greater resistance to thermal changes and chemical corrosion.
It has greater resistance to thermal shock and allows for greater accuracy in laboratory measurements when heating and cooling experiments
It is used for
  Laboratories
  Industrial chemical process plants
  In the pharmaceutical industry
  Domestic kitchens
  In bulbs for high-powered lamps

## Slide 19
Aluminosilicate Glass
Composition: Aluminum oxide
It is used as resistors for electronic circuitry
It is similar to borosilicate glass but it has:
Greater chemical durability
Can withstand higher operating temperatures
Are more difficult to fabricate

## Slide 20
It is resistant to heat shock up to 900°C.
Ninety-six percent silica glass
Is a borosilicate glass melted, then processed to remove almost all the non-silicate elements from the piece
Furnace glass, for out windows on space vehicles

## Slide 21
It can sustain temperatures up to 1200°C for short periods
Pure silicon dioxide in non-crystalline state
Very difficult to fabricate, most expensive of all glasses
Crucibles for growing crystals
Fused silica glass

## Slide 22
Importance
Glass is considered a very important element in the arsenal of Architects and Interior Designers. It is also pondered an important element in the exuberance of available construction materials.
New varieties have been developed to aid designers, and are being used in a number of creative ways to enhance the aesthetic beauty of the space.
They are an excellent material for:
  Acoustic & thermal insulation
  Water-proofing
  Abrasion resistance
  Being a bad conductor of heat gives the use of glass a new practical application in the form of energy-conservation, which makes glass more dulcifying.

## Slide 23
With their improved strength, pressure and impact resistance, heat and water-proof characteristics, glass blocks can be used either to construct the walls separately, or used freely for decorative purposes.
Glass blocks can be shifted and collocated freely with other shapes or colors to meet various demands of different applications.
Transparent glass blocks can be used for interior divisions as they have an excellent lighting performance and seem to extend the available space.
Importance

## Slide 24: Conclusion
Today, glass is used all over the world. A designer’s pursuit for transparency, weightlessness and luminosity has been fulfilled by Glass. Most major projects around the world use glass in some way to add beauty to buildings and create astounding pieces of art. Glass is taking the world of architecture and interiors by storm.

## Slide 25: References
Architectural glass. (2007). In Encyclopædia Britannica. Retrieved February 6, 2007, from Britannica Concise Encyclopedia: http://concise.britannica.com/ebc/article-9365670/architectural-glass
glassware. (2007). In Encyclopædia Britannica. Retrieved February 6, 2007, from Encyclopædia Britannica Online: http://www.britannica.com/eb/article-74238
http://supermanlee.com/mg448fall2010/joan/p.iii.history.html
http://www.crystalartusa.com/typesofglass.aspx